## Slide 1
Congestion Control
in Data Centers (I)
H. Jonathan Chao
ECE Department
chao@nyu.edu

## Slide 2: TCP in the Data Center (DC)
TCP does not meet demands of DC applications.
  TCP requires large queues for high throughput. However, it
    adds significant latency
    wastes buffer space
    performs bad with shallow-buffered switches
DC operators work around the TCP problems, by
  Using Ad-hoc, inefficient, often expensive solutions, e.g., reducing Retransmission TimeOut (RTO) timer’s value, without fully understanding of consequences, tradeoffs.

## Slide 3: How does search work?
TLA
(Top-level Aggregator)
MLA
(Mid-level Aggregator)
MLA
Worker Nodes
………
Picasso
“Everything you can imagine is real.”
“Bad artists copy.
Good artists steal.”
“It is your work in life that is the ultimate seduction.“
“The chief enemy of creativity is good sense.“
“Inspiration does exist,
but it must find you working.”
“I'd like to live as a poor man
with lots of money.“
“Art is a lie that makes us
realize the truth.
“Computers are useless.
They can only give you answers.”
1.
2.
3.
…..
1. Art is a lie…
2. The chief…
3.
…..
1.
2. Art is a lie…
3.
…..
Art is…
Picasso
Time is money
  Strict deadlines
  Service-level
  Agreements (SLAs)
Missed deadline
  Low service quality result
Many requests per query
  Tail-latency matters
Deadline = 250ms
Deadline = 50ms
Deadline = 10ms
Partition/Aggregate Application Structure
Notes: After the animation, say “this follows what we call the partition/aggregate application structure. It’s actually quite general any time you have to do distributed lookups of large data structures to resolve queries.”
TLA: Top-level aggregators
MLA: Mid-level aggregator

## Slide 4: Data Center Workloads
Partition/Aggregate
(Query)
Short messages [50KB-1MB]
(Coordination, Control state)
Large flows [1MB-100MB]
(Data update)
Bursty, Delay-sensitive
Delay-sensitive
Throughput-sensitive
Notes: Replace PDF

## Slide 5: Flow Size Distribution
> 65% of Flows are < 1MB
> 95% of Bytes from Flows > 1MB

## Slide 6: Incast meeting with shallow buffers
TCP timeout
Worker 1
Worker 2
Worker 3
Worker 4
Aggregator
RTOmin = 300 ms
(Retransmission TimeOut)
Synchronized fan-in congestion:
  Caused by Partition/Aggregate.
Vasudevan et al. (SIGCOMM’09)

## Slide 7: Queue Buildup
Sender 1
Sender 2
Receiver
Large flows buildup queues.
Measurements in Bing cluster
  For 90% packets: RTT < 1ms
  For 10% packets: 1ms < RTT < 15ms
  Large flows result in the increase of short flows’ latency

## Slide 8: Data Center Transport Requirements
High Burst Tolerance
  Incast due to Partition/Aggregate is common
Low Latency
  Short flows, queries
3. High Throughput
  Continuous data updates, large file transfers
The challenge is to achieve these three together.

## Slide 9: The TCP Control Loop with ECN Mark
Sender 1
Sender 2
Receiver
ECN Mark (1 bit)
ECN = Explicit Congestion Notification
Time
Window Size (Rate)
Additive Increase:
W  W+1 per round-trip time
Multiplicative Decrease:
W  W/2 per drop or ECN mark
Notes: DCTCP is based on the existing Explicit Congestion Notification framework in TCP.

## Slide 10: TCP Buffer Sizing & Latency
10G x RTT
1G x RTT
Buffer Size
Time
Widespread conception: increase link speed to reduce latency
  Eg. upgrade from 1Gbps to 10Gbps network.
However, increasing link speed doesn’t lower queuing delay, because:
  Switch buffers also need to be 10 times larger and 10 times faster.
1G
10G
Notes: why times larger and 10 times faster?

## Slide 11: DCTCP (Data Center TCP)

## Slide 12: DCTCP: Main Idea
React in proportion to the extent of congestion.
  Reduce window size based on fraction of marked packets.
ECN Marks | TCP | DCTCP
1 0 1 1 1 1 0 1 1 1 | Cut window by 50% | Cut window by 40%
0 0 0 0 0 0 0 0 0 1 | Cut window by 50% | Cut window by 5%
Notes: Start with: “How can we extract multi-bit information from single-bit stream of ECN marks?”

## Slide 13: DCTCP: Algorithm
Switch side:
  Mark packets when Queue Length > K.
  Sender side:
  Maintain running average of fraction of packets marked (α).
Adaptive window decreases:
  Note: between 0 and 1
B
K
Mark
Don’t
Mark
Notes: very simple marking mechanism
not all the tunings other aqms have
on the source side, the source is trying to estimate the fraction of packets getting marked
using the obs that there is a stream of ecn marks coming back – more info in the stream than in any single bit
trying to maintain smooth rate variations to operate well even when using shallow buffers, and only a few flows (no stat mux)
F over the last RTT. In TCP there is always a way to get the next RTT from the window size. Comes from the self-clocking of TCP.
Only changing the decrease. Simplest version – makes a lot of sense. So generic could apply it to any algorithm – CTCP, CUBIC – how to cut its window leaving increase part to what it already does. Have to be careful here.

## Slide 14: DCTCP vs TCP
Setup: Win 7, Broadcom 1Gbps Switch
Scenario: 2 long-lived flows,
(Kbytes)
ECN Marking Thresh = 30KB
(i.e., 20 * 1.5KB packets)
Notes: Not ns2.

## Slide 15: Evaluation
Implemented in Windows stack.
Real hardware, 1Gbps and 10Gbps experiments
  90 server testbed
  Broadcom Triumph 48 1G ports – 4MB shared memory
  Cisco Cat4948 48 1G ports – 16MB shared memory
  Broadcom Scorpion 24 10G ports – 4MB shared memory
Numerous micro-benchmarks
  – Throughput and Queue Length
  – Multi-hop
  – Queue Buildup
  – Buffer Pressure
Bing cluster benchmark
– Fairness and Convergence
– Incast
– Static vs Dynamic Buffer Mgmt

## Slide 16: Bing Benchmark (Scaled 10x)
Query Traffic
(Bursty)
Short messages
(Delay-sensitive)
Completion Time (ms)
incast
Deep buffers fixes incast, but makes latency worse
DCTCP good for both incast & latency

## Slide 17: Convergence Time
Convergence time: the time required for a new flow to grab its share of the bandwidth from an existing flow with a large window size.
DCTCP trades off convergence time because it makes more fine-grained adjustments to the window than TCP
At most ~40% more RTTs than TCP
  Alizadeh et al. “Analysis of DCTCP: Stability, Convergence, and Fairness,” SIGMETRICS 2011.
  Fortunately, RTT in data center is very small (e.g., hundreds of microseconds)
Intuition: DCTCP makes small multiplicative decreases, but makes them much more frequently than TCP
Notes: In the first part of the talk, we established that what we need from DCTCP is to maintain small queues, without loss of throughput
Now in the case of TCP, the question of how much buffering is needed for high throughput has been studied and is known in the literature as the buffer sizing problem.
… and I’ll show you how to get low var…
convergence time; the time required for a new flow to
grab its share of the bandwidth from an existing flow with a
large window size.