## Slide 1
Software Defined Networking (SDN)
H. Jonathan Chao
ECE Department
chao@nyu.edu

## Slide 2: Outline
Limitations of Current Networks
Software Defined Networking (SDN) Concept
Why SDN?
SDN Control Plane
SDN Data Plane
SDN Use Cases

## Slide 3: 1. Limitations of Current Networks

## Slide 4: Limitations of Current Networks
Old ways to configure a network
Specialized Packet Forwarding Hardware
App
App
App
Specialized Packet Forwarding Hardware
App
App
App
Specialized Packet Forwarding Hardware
App
App
App
Specialized Packet Forwarding Hardware
App
App
App
Specialized Packet Forwarding Hardware
Operating
System
Operating
System
Operating
System
Operating
System
Operating
System
App
App
App
OpenFlow/SDN tutorial, Srini Seetharaman, Deutsche Telekom, Silicon Valley Innovation Center

## Slide 5: Limitations of Current Networks
Million of lines of source code
Billions of gates
Many complex functions baked into infrastructure
    OSPF, BGP, multicast, differentiated services, Traffic Engineering, NAT, firewalls, …
Specialized Packet Forwarding Hardware
Operating
System
Feature
Feature
OpenFlow/SDN tutorial, Srini Seetharaman, Deutsche Telekom, Silicon Valley Innovation Center
Cannot dynamically change according to network conditions

## Slide 6: Limitations of Current Networks
Networks are difficult to manage
  Many switches / service
  Manual management and configuration of individual elements
  Man power required for network maintenance
  Complexity of automated configuration to deal with non-standard vendor configuration APIs
New control requirements have arisen
  Greater scale
  Migration of virtual machines (VMs)
  Chain of middleboxes for various policies
Current equipment and protocols have limitations
  Little support for monitoring and operations
  Optimized for “eventual consistency” in routing
  Little baseline support for low latency routing and fast failover
How to easily manage huge networks?
  Need observability (global network view) and controllability (per flow routing)
  SDN achieves these capabilities
Notes: validate responsiveness as demand varies according to user needs
firewalls and load balancers
eliminate vulnerability and exposure between users and applications

## Slide 7
Vertically integrated
Closed, proprietary
Slow innovation
Small industry
Specialized
Operating
System
Specialized
Hardware
App
App
App
App
App
App
App
App
App
App
App
Specialized
Applications
Horizontal
Open interfaces
Rapid innovation
Huge industry
Microprocessor
Open Interface
Linux
Mac
OS
Windows
(OS)
or
or
Open Interface
Computer System

## Slide 8
Vertically integrated
Closed, proprietary
Slow innovation
App
App
App
App
App
App
App
App
App
App
App
Horizontal
Open interfaces
Rapid innovation
Control
Plane
Control
Plane
Control
Plane
or
or
Open Interface
Specialized
Control
Plane
Specialized
Hardware
Specialized
Features
Merchant
Switching Chips
Open Interface
Network System

## Slide 9: 2. What is Software Defined Networking (SDN)?

## Slide 10: Idea: An OS for Networks
Specialized Packet Forwarding Hardware
App
App
App
Specialized Packet Forwarding Hardware
App
App
App
Specialized Packet Forwarding Hardware
App
App
App
Specialized Packet Forwarding Hardware
App
App
App
Specialized Packet Forwarding Hardware
Operating
System
Operating
System
Operating
System
Operating
System
Operating
System
App
App
App
Closed
OpenFlow/SDN tutorial, Srini Seetharaman, Deutsche Telekom, Silicon Valley Innovation Center

## Slide 11: Idea: An OS for Networks
Specialized Packet Forwarding Hardware
App
App
App
Specialized Packet Forwarding Hardware
App
App
App
Specialized Packet Forwarding Hardware
App
App
App
Specialized Packet Forwarding Hardware
App
App
App
Specialized Packet Forwarding Hardware
Operating
System
Operating
System
Operating
System
Operating
System
Operating
System
App
App
App
Network Operating System
Control Programs
OpenFlow/SDN tutorial, Srini Seetharaman, Deutsche Telekom, Silicon Valley Innovation Center
Notes: How do we redefine the architecture to open up networking infrastructure and the industry!
By bring to the networking industry what we did to the computing world

## Slide 12: Idea: An OS for Networks
Simple Packet Forwarding Hardware
Simple Packet Forwarding Hardware
Simple Packet Forwarding Hardware
Simple Packet Forwarding Hardware
Simple Packet Forwarding Hardware
Network Operating System
Control Programs
OpenFlow/SDN tutorial, Srini Seetharaman, Deutsche Telekom, Silicon Valley Innovation Center
Notes: The key is to have a standardized control interface that speaks directly to hardware
A whole network is like a big machine

## Slide 13: Idea: An OS for Networks
“NOX: Towards an Operating System for Networks”
Global Network View
Protocols
Protocols
Control via forwarding
interface
Network Operating System
Control Programs
Software-Defined Networking (SDN)
The Future of Networking, and the Past of Protocols, Scott Shenker, with Martin Casado, Teemu Koponen, Nick McKeown
Notes: A remote controller has control of a switch’s forwarding decisions

## Slide 14: 3. Why SDN?

## Slide 15: Network-layer functions
Two approaches to structuring network control plane:
per-router control (traditional)
logically centralized control (software defined networking)
forwarding: move packets from router’s input to appropriate router output
data plane
control plane
routing: determine route taken by packets from source to destination
For the rest of slides, most are from “Computer Networking: A Top-Down Approach” “8th edition, Jim Kurose, Keith Ross, Chapters 4& 5, http://gaia.cs.umass.edu/kurose_ross/ppt.htm

## Slide 16: Per-router control plane
Individual routing algorithm components in each and every router interact in the control plane
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header
3

## Slide 17: Software-Defined Networking (SDN) control plane
Remote controller computes, installs forwarding tables in routers
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1
2
0111
3
values in arriving
packet header
Control Agent

## Slide 18: Software defined networking (SDN)
Internet network layer: historically implemented via distributed, per-router control approach:
  monolithic router contains switching hardware, runs proprietary implementation of Internet standard protocols (IP, RIP, IS-IS, OSPF, BGP) in proprietary router OS (e.g., Cisco IOS)
  different “middleboxes” for different network layer functions: firewalls, load balancers, NAT boxes, ..
~2005: renewed interest in rethinking network control plane

## Slide 19: Middleboxes everywhere!
enterprise
network
national or global ISP
datacenter
network
NAT: home, cellular, institutional
Firewalls, IDS: corporate, institutional, service providers, ISPs
Load balancers: corporate, service provider, data center, mobile nets
Caches: service provider, mobile, CDNs
Application-specific: service providers, institutional, CDN

## Slide 20: Middleboxes
initially: proprietary (closed) hardware solutions
move towards “whitebox” hardware implementing open API
  move away from proprietary hardware solutions
  programmable local actions via match+action
  move towards innovation/differentiation in software
SDN: (logically) centralized control and configuration management often in private/public cloud
network functions virtualization (NFV): programmable services over white box networking, computation, storage

## Slide 21: Middleboxes
A middlebox or network appliance is a computer networking device that transforms, inspects, filters, or otherwise manipulates traffic for purposes other than packet forwarding. Common examples of middleboxes include firewalls, which filter unwanted or malicious traffic, and network address translators (NAT), which modify packets' source and destination addresses.
Dedicated middlebox hardware is widely deployed in enterprise networks to improve network security and performance, however, even home network routers often have integrated firewall, NAT, or other middlebox functionality.
In enterprise networks, hardware modules enforce policies on flows
  Higher throughput in comparison to software
  Modifying every end host to enforce policies is not scalable and it lacks flexibility
  But, where to place middleboxes?
https://en.wikipedia.org/wiki/Middlebox

## Slide 22: Types of Middleboxes
Firewalls filter traffic based on a set of pre-defined security rules defined by a network administrator. IP firewalls reject packets "based purely on fields in the IP and Transport headers (e.g. disallow incoming traffic to certain port numbers, disallow any traffic to certain subnets etc.)" Other types of firewalls may use more complex rulesets, including those that inspect traffic at the session or application layer.
Intrusion Detection Systems monitor traffic and collect data for offline analysis for security anomalies. Because IDSs unlike firewalls do not filter packets in real-time, they traditionally are capable of more complex inspection than firewalls which must make an accept/reject decision about each packet as it arrives.
Network Address Translators replace the source and/or destination IP addresses of packets that traverse them. Typically, NATs are deployed to allow multiple end hosts to share a single IP address: hosts "behind" the NAT are assigned a private IP address and their packets destined to the public Internet traverse a NAT which replaces their internal, private address with a shared public address.
WAN Optimizers improve bandwidth consumption and perceived latency between dedicated endpoints. Typically deployed in large enterprises, WAN optimizers are deployed near both sending and receiving endpoints of communication; the devices then co-ordinate to cache and compress traffic that traverses the Internet.
Load balancers provide one point of entry to a service, but forward traffic flows to one or more hosts that actually provide the service.
https://en.wikipedia.org/wiki/Middlebox

## Slide 23: Chaining Middleboxes in a Data Center
Packets pass through middleboxes (firewall, network address translator, load balancer) before reaching the destination
chaining of various middleboxes – needs to be flexible, agile, and fast configuration
Middleboxes
Datacenter
Internet traffic

## Slide 24: Software defined networking (SDN)
Why a logically centralized control plane?
easier network management: avoid router misconfigurations, greater flexibility of traffic flows
table-based forwarding allows “programming” routers
  centralized “programming” easier: compute tables centrally and distribute
  distributed “programming” more difficult: compute tables as result of distributed algorithm (protocol) implemented in each-and-every router
open (non-proprietary) implementation of control plane
  foster innovation: let 1000 flowers bloom

## Slide 25: Traffic engineering: difficult with traditional routing
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
Q: what if network operator wants u-to-z traffic to flow along uvwz, rather than uxyz?
A: need to re-define link weights so traffic routing algorithm computes routes accordingly (or need a new routing algorithm)!
link weights are only control “knobs”: not much control!

## Slide 26: Traffic engineering: difficult with traditional routing
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
Q: what if network operator wants to split u-to-z traffic along uvwz and uxyz (load balancing)?
A: can’t do it (or need a new routing algorithm)

## Slide 27: Traffic engineering: difficult with traditional routing
Q: what if w wants to route blue and red traffic differently from w to z?
A: can’t do it (with destination-based forwarding, and LS, DV routing)
2
2
1
3
1
1
2
5
3
5
v
w
u
z
y
x
We learned in Chapter 4 that generalized forwarding and SDN can be used to achieve any routing desired

## Slide 28: Software defined networking (SDN)
data
plane
control
plane
Remote Controller
CA
CA
CA
CA
CA
1: generalized “flow-based” forwarding (e.g., OpenFlow)
2. control, data plane separation
3. control plane functions external to data-plane switches
…
routing
access control
load
balance
4. programmable control applications

## Slide 29: 4. SDN Control Plane

## Slide 30: Software defined networking (SDN)
Data-plane switches:
fast, simple, commodity switches implementing generalized data-plane forwarding in hardware
flow (forwarding) table computed, installed under controller supervision
API for table-based switch control (e.g., OpenFlow)
  defines what is controllable, what is not
protocol for communicating with controller (e.g., OpenFlow)
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 31: Software defined networking (SDN)
SDN controller (network OS):
maintain network state information
interacts with network control applications “above” via northbound API
interacts with network switches “below” via southbound API
implemented as distributed system for performance, scalability, fault-tolerance, robustness
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 32: Software defined networking (SDN)
network-control apps:
“brains” of control: implement control functions using lower-level services, API provided by SDN controller
unbundled: can be provided by 3rd party: distinct from routing vendor, or SDN controller
data
plane
control
plane
SDN Controller
(network operating system)
…
routing
access
control
load
balance
southbound API
northbound API
SDN-controlled switches
network-control applications

## Slide 33: Components of SDN controller
Network-wide distributed, robust state management
Communication to/from controlled devices
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Interface, abstractions for network control apps
SDN
controller
routing
access
control
load
balance
communication: communicate between SDN controller and controlled switches
network-wide state management : state of networks links, switches, services: a distributed database
interface layer to network control apps: abstractions API

## Slide 34: SDN Controller
SDN controllers of a datacenter provide policy and centralized managements for the Openstack Neutron networking layer that provides inter-working between the virtual ports created by Nova.
  Nova, an OpenStack project, provides a way to provision VMs.
Historical SDN controllers for managing the programmable switches of the network.
  SDN controllers is to manage the Linux kernel features made of L3 IP routing, Linux bridges, iptables or ebtables, network namespaces and Open vSwitch.
Open and community driven initiatives the following SDN controllers: Open Daylight (controller baseline project upon which many other controllers are built), ONOS, Project Calico, The Fast Data Project, Project Floodlight, Beacon, NOX/POX, Open vSwitch, vneio/sdnc (SDN Controller from vne.io), Ryu Controller (supported by NTT Labs), Cherry, Faucet (Python based on Ryu for production networks), OpenContrail
https://en.wikipedia.org/wiki/List_of_SDN_controller_software

## Slide 35: SDN Controller - Ryu
Ryu Controller is an open, software-defined networking (SDN) Controller designed to increase the agility of the network by making it easy to manage and adapt how traffic is handled. In general, the SDN Controller is the brains of the SDN environment, communicating information down to the switches and routers with southbound APIs, and up to the applications and business logic with northbound APIs. The Ryu Controller is supported by NTT and is deployed in NTT cloud data centers as well.
The Ryu Controller provides software components, with well-defined application program interfaces (APIs), that make it easy for developers to create new network management and control applications. This component approach helps organizations customize deployments to meet their specific needs; developers can quickly and easily modify existing components or implement their own to ensure the underlying network can meet the changing demands of their applications.
https://www.sdxcentral.com/sdn/definitions/sdn-controllers/open-source-sdn-controllers/what-is-ryu-controller/

## Slide 36
The Ryu Controller source code is hosted on GitHub and managed and maintained by the open Ryu community. OpenStack, which runs an open collaboration focused on developing a cloud operating system that can control the compute, storage and networking resources of an organization, supports deployments of Ryu as the network Controller.
Written entirely in Python, all of Ryu’s code is available under the Apache 2.0 license and open for anyone to use. The Ryu Controller supports NETCONF and OF-config network management protocols, as well as OpenFlow, which is one of the first and most widely deployed SDN communications standards.
The Ryu Controller can use OpenFlow to interact with the forwarding plane (switches and routers) to modify how the network will handle traffic flows. It has been tested and certified to work with a number of OpenFlow switches, including Open vSwitch and offerings from Centec, Hewlett Packard, IBM, and NEC.
https://www.sdxcentral.com/sdn/definitions/sdn-controllers/open-source-sdn-controllers/what-is-ryu-controller/

## Slide 37: OpenFlow protocol
operates between controller, switch
TCP used to exchange messages
  optional encryption
three classes of OpenFlow messages:
  controller-to-switch
  asynchronous (switch to controller)
  symmetric (misc.)
distinct from OpenFlow API
  API used to specify generalized forwarding actions
OpenFlow Controller

## Slide 38: OpenFlow: controller-to-switch messages
Key controller-to-switch messages:
features: controller queries switch features, switch replies
configure: controller queries/sets switch configuration parameters
modify-state: add, delete, modify flow entries in the OpenFlow tables
packet-out: a message used by the controller to send out a specific packet out of a specific switch port
OpenFlow Controller

## Slide 39: OpenFlow: switch-to-controller messages
Key switch-to-controller messages
packet-in: a not-matched packet sent to controller for further processing (e.g., routing), or a matched packet in some cases
flow-removed: flow table entry deleted at switch
port status: inform controller of a change on a port.
Fortunately, network operators don’t “program” switches by creating/sending OpenFlow messages directly. Instead use higher-level abstraction at controller
OpenFlow Controller

## Slide 40: OpenFlow Messages
Asynchronous (Controller-to-Switch)
  Send-packet: to send packet out of a specific port on a switch
  Flow-mod: to add/delete/modify flows in the flow table
Asynchronous (initiated by the controller)
  Read-state: to collect statistics about flow table, ports and individual flows
  Features: sent by controller when a switch connects to find out the features supported by a switch
  Configuration: to set and query configuration parameters in the switch
Asynchronous (initiated by the switch)
  Packet-in: for all packets that do not have a matching rule, this event is sent to controller
  Flow-removed: whenever a flow rule expires, the controller is sent a flow-removed message
  Port-status: whenever a port configuration or state changes, a message is sent to controller
  Error: error messages
Symmetric (can be sent in either direction without solicitation)
  Hello: at connection startup
  Echo: to indicate latency, bandwidth or liveliness of a controller-switch connection
  Vendor: for extensions (that can be included in later OpenFlow versions)
Theophilus Benson, CPS 590: Software Defined Networking, https://www.cs.duke.edu/courses/fall14/compsci590.4/notes/F14_Class1.pptx

## Slide 41: SDN: control/data plane interaction example
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Dijkstra’s link-state
routing
s1
s2
s3
s4
S1, experiencing link failure to S2 uses OpenFlow port status message to notify controller
1
SDN controller receives OpenFlow message, updates link status info
2
Dijkstra’s routing algorithm application has previously registered to be called when ever link status changes. It is called.
3
Dijkstra’s routing algorithm access network graph info, link state info in controller, computes new routes
4
1
2
3
4

## Slide 42: SDN: control/data plane interaction example
Link-state info
switch info
host info
statistics
flow tables
…
…
OpenFlow
SNMP
…
network graph
intent
RESTful
API
…
Dijkstra’s link-state
routing
s1
s2
s3
s4
link state routing app interacts with flow-table-computation component in SDN controller, which computes new flow tables needed
5
controller uses OpenFlow to install new tables in switches that need updating
S1 will now route packets destined to S2 via S4
6
5
6
1
2
3
4

## Slide 43: 5. SDN Data Plane

## Slide 44: Generalized forwarding: match plus action
1
2
0111
3
values in arriving
packet header
Review: each router contains a forwarding table
“match plus action” abstraction: match bits in arriving packet, take action
  generalized forwarding:
    many header fields can determine action
    many action possible: drop/copy/modify/log packet
forwarding table
(aka: flow table)
(aka: flow table)
  destination-based forwarding: forward based on dest. IP address

## Slide 45: Flow table abstraction
flow: defined by header field values (in link-, network-, transport-layer fields)
generalized forwarding: simple packet-handling rules
  match: pattern values in packet header fields
  actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  priority: disambiguate overlapping patterns
  counters: #bytes and #packets
Router’s flow table define router’s match+action rules
Flow table
match
action

## Slide 46: Flow table abstraction
flow: defined by header fields
generalized forwarding: simple packet-handling rules
  match: pattern values in packet header fields
  actions: for matched packet: drop, forward, modify, matched packet or send matched packet to controller
  priority: disambiguate overlapping patterns
  counters: #bytes and #packets
Flow table
match
action
1
2
3
4
* : wildcard
src=10.1.2.3, dest=*.*.*.* send to controller
src=1.2.*.*, dest=*.*.*.* drop
src = *.*.*.*, dest=3.4.*.* forward(2)

## Slide 47: OpenFlow Usage
Controller
PC
OpenFlow Switch
OpenFlow Switch
OpenFlow Switch
Alice’s code
Decision?
OpenFlow
Protocol
Alice’s Rule
Alice’s Rule
Alice’s Rule
OpenFlow/SDN tutorial, Srini Seetharaman, Deutsche Telekom, Silicon Valley Innovation Center
Alice’s code:
  Simple learning switch
  Per Flow switching
  Network access control/firewall
  Static “VLANs”
  Her own new routing protocol: unicast, multicast, multipath
  Home network manager
  Packet processor (in controller)
  IPvAlice
Notes: Table entries can be updated

## Slide 48: OpenFlow facilitates SDN
Controller(NOS)
Applications
Applications
Applications
Southbound
API
Switch H.W
Switch O.S
Switch H.W
Switch O.S
OpenFlow
OpenFlow
Theophilus Benson, CPS 590: Software Defined Networking, https://www.cs.duke.edu/courses/fall14/compsci590.4/notes/F14_Class1.pptx

## Slide 49: OpenFlow
Data Path (Hardware)
Control Path
OpenFlow
OpenFlow Controller
OpenFlow Protocol (SSL/TCP)
OpenFlow/SDN tutorial, Srini Seetharaman, Deutsche Telekom, Silicon Valley Innovation Center
Switch/Router
Notes: Leverages hardware inside most switches today (ACL tables)

## Slide 50
The Stanford Clean Slate Program, http://cleanslate.stanford.edu
Controller
PC
Hardware
Layer
Software
Layer
OpenFlow Table
MAC
src
MAC
dst
IP
Src
IP
Dst
TCP
sport
TCP
dport
Action
OpenFlow Client
*
*
5.6.7.8
*
*
*
port 1
port 4
port 3
port 2
port 1
1.2.3.4
5.6.7.8
Switch
TCAM
Switch/Router
TCAM: Ternary Content
Addressable Memory

## Slide 51: OpenFlow: flow table entries
Match
Action
Stats
Forward packet to port(s)
Drop packet
Modify fields in header(s)
Encapsulate and forward to controller
Packet + byte counters
Header fields to match:
Ingress Port
Src MAC
Dst MAC
Eth Type
VLAN
ID
IP
ToS
IP Proto
IP Src
IP Dst
TCP/UDP Src Port
VLAN
Pri
TCP/UDP Dst Port
Link layer
Network layer
Transport layer

## Slide 52: OpenFlow: examples
IP datagrams destined to IP address 51.6.0.8 should be forwarded to router output port 6
Block (do not forward) all datagrams destined to TCP port 22 (ssh port #)
Block (do not forward) all datagrams sent by host 128.119.1.1
Destination-based forwarding:
*
*
*
*
*
*
51.6.0.8
*
*
*
port6
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
*
*
*
*
*
*
*
*
*
*
*
*
Firewall:
drop
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
22
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS
*
*
*
*
*
*
*
*
*
*
drop
*
128.119.1.1

## Slide 53: OpenFlow: examples
Layer 2 destination-based forwarding:
layer 2 frames with destination MAC address 22:A7:23:11:E1:02 should be forwarded to output port 3
*
*
*
*
*
*
*
*
*
port3
22:A7:23:
11:E1:02
*
*
Switch
Port
MAC
src
MAC
dst
Eth
type
VLAN
ID
IP
Src
IP
Dst
IP
Prot
TCP
s-port
TCP
d-port
Action
VLAN
Pri
IP
ToS

## Slide 54: OpenFlow abstraction
match+action: abstraction unifies different kinds of devices
Router
  match: longest destination IP prefix
  action: forward out a link
Switch
  match: destination MAC address
  action: forward or flood
Firewall
  match: IP addresses and TCP/UDP port numbers
  action: permit or deny
NAT
  match: IP address and port
  action: rewrite address and port

## Slide 55: Generalized forwarding: summary
“match plus action” abstraction: match bits in arriving packet header(s) in any layers, take action
  matching over many fields (link-, network-, transport-layer)
  local actions: drop, forward, modify, or send matched packet to controller
  “program” network-wide behaviors
simple form of “network programmability”
  programmable, per-packet “processing”
  historical roots: active networking
  today: more generalized programming:
  P4 (see p4.org).

## Slide 56: 6. SDN Use Cases

## Slide 57: OpenFlow example
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Orchestrated tables can create network-wide behavior, e.g.,:
datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2

## Slide 58: OpenFlow example
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(3)
match
action
ingress port = 2
IP Dst = 10.2.0.3
ingress port = 2
IP Dst = 10.2.0.4
forward(3)
match
action
forward(4)
ingress port = 1
IP Src = 10.3.*.*
IP Dst = 10.2.*.*
forward(4)
match
action
Host h1
10.1.0.1
Host h2
10.1.0.2
Host h4
10.2.0.4
Host h3
10.2.0.3
Host h5
10.3.0.5
s1
s2
s3
1
2
3
4
1
2
3
4
1
2
3
4
Host h6
10.3.0.6
controller
Orchestrated tables can create network-wide behavior, e.g.,:
datagrams from hosts h5 and h6 should be sent to h3 or h4, via s1 and from there to s2

## Slide 59: SDN: selected challenges
hardening the control plane: dependable, reliable, performance-scalable, secure distributed system
  robustness to failures: leverage strong theory of reliable distributed system for control plane
  dependability, security: “baked in” from day one?
networks, protocols meeting mission-specific requirements
  e.g., real-time, ultra-reliable, ultra-secure
Internet-scaling: beyond a single Autonomous System (AS)
SDN critical in 5G cellular networks

## Slide 60: Data-Plane Limitations
Limited Number of TCAM entries
  Currently only 1K
    Networks have more than 1K flows
  How to fit network in limited entries?
Limited control channel capacity
  All switches use the same controller interface
  Need to rate limit control messages
    Prioritize certain messages
Limited switch CPU
  Less power than a smartphone 
  Limit control messages and actions that use CPU
Controller (N. O.S.)
Applications
Applications
Applications
Switch H.W
O.S
Theophilus Benson, CPS 590: Software Defined Networking, https://www.cs.duke.edu/courses/fall14/compsci590.4/notes/F14_Class1.pptx

## Slide 61: Debugging SDNs
Problems can occur anywhere in the SDN stack
  How do you diagnose each type of problem?
Network O.S.
Applications
Applications
Applications
Switch Operating System
Switch Hardware
Buggy
App
Buggy
NOS
Switch Operating System
Switch Hardware
Buggy
Switch
H/W
Buggy
Switch
S/W
Theophilus Benson, CPS 590: Software Defined Networking, https://www.cs.duke.edu/courses/fall14/compsci590.4/notes/F14_Class1.pptx

## Slide 62: SDN and the future of traditional network protocols
SDN-computed versus router-computer forwarding tables:
  just one example of logically-centralized-computed versus protocol computed
one could imagine SDN-computed congestion control:
  controller sets sender rates based on router-reported (to controller) congestion levels
How will implementation of network functionality (SDN versus protocols) evolve?

## Slide 63: Conclusions
What is SDN and Why?
  A system-layered abstraction
  Programmable, flexible, and extensible
What is OpenFlow?
  Interface between switches and controllers
  Enabling SDN
SDN is here for real-world use
  Enables rapid rich feature deployment
  Simplifies network management