## Slide 1: CONGA: Distributed Congestion-Aware Load Balancing for Datacenters
Mohammad Alizadeh
Tom Edsall, Sarang Dharmapurikar, Ramanan Vaidyanathan, Kevin Chu, Andy Fingerhut, Vinh The Lam★, Francis Matus, Rong Pan, Navindra Yadav, George Varghese§
★
§
Notes: I’m going to be talking today about work that we’ve been doing over the past couple years on a new load balancing mechanism for datacenter networks.
This is joint work with my colleagues at Cisco, as well as Terry Lam at Google and George Varghese at Microsoft.

## Slide 2: Motivation
Leaf
1000s of server ports
Multi-rooted tree [Fat-tree, Leaf-Spine, …]
Full bisection bandwidth, achieved via multipathing
Spine
Access
Single-rooted tree
High oversubscription
1000s of server ports
Agg
Core
DC networks need large bisection bandwidth for distributed apps (big data, HPC, web services, etc)
Notes: To set the context, the primary motivation for this work is that datacenter networks need to provide large amounts of bisection bandwidth to support distributed applications; if you consider applications like big data analytics, hPC, or web services, they all require significant network IO between components that are spread across 100s or even 1000s of servers.
In response to this, in recent years, the single rooted tree topologies that have been used in enterprise networks for decades are being replaced with multi-rooted topologies. These new topologies, also called fat-tree or Leaf-Spine, are great -- they can scale bandwidth arbitrarily by just adding more paths; for example, adding more spine switches in a Leaf-Spine design.

## Slide 3: Motivation
Leaf
1000s of server ports
Multi-rooted tree [Fat-tree, Leaf-Spine, …]
Full bisection bandwidth, achieved via multipathing
Spine
DC networks need large bisection bandwidth for distributed apps (big data, HPC, web services, etc)
Notes: So the whole industry is moving in this direction -- of using multi-rooted topologies to build networks with full or near-full bisection bandwidth.
This is great… but if we take a step back, it’s not really what we want.

## Slide 4: Multi-rooted != Ideal DC Network
1000s of server ports
Ideal DC network:
Big output-queued switch
No internal bottlenecks  predictable
Simplifies BW management [EyeQ, FairCloud, pFabric, Varys, …]
Multi-rooted tree
1000s of server ports
Can’t build it 
≈
Possible
bottlenecks
Need precise load balancing
Notes: A multi-rooted topology is not the “ideal” datacenter network.
What is the ideal network? The ideal network would be a big switch – or more precisely a big output-queued switch. That’s a switch that whenever…

## Slide 5: Today: ECMP Load Balancing
Pick among equal-cost paths by a hash of 5-tuple
Approximates Valiant load balancing
Preserves packet order
Problems:
Hash collisions
(coarse granularity)
Local & stateless
(v. bad with asymmetry
due to link failures)
H(f) % 3 = 0
Notes: Valiant load balancing http://yuba.stanford.edu/vlb/

## Slide 6: Dealing with Asymmetry
40G
40G
40G
40G
40G
40G
Handling asymmetry needs non-local knowledge

## Slide 7: Dealing with Asymmetry
40G
40G
40G
40G
40G
Handling asymmetry needs non-local knowledge
30G
30G
(UDP)
40G
(TCP)
Scheme | Thrput
ECMP (Local Stateless) | 
Local Cong-Aware | 
Global Cong-Aware | 

## Slide 8: Dealing with Asymmetry: ECMP
40G
40G
40G
40G
40G
30G
20G
20G
30G
(UDP)
40G
(TCP)
Scheme | Thrput
ECMP (Local Stateless) | 
Local Cong-Aware | 
Global Cong-Aware | 
10G
60G

## Slide 9: Dealing with Asymmetry: Local Congestion-Aware
40G
40G
40G
40G
40G
30G
20G
30G
(UDP)
40G
(TCP)
Scheme | Thrput
ECMP (Local Stateless) | 
Local Cong-Aware | 
Global Cong-Aware | 
10G
60G
10G
50G
Interacts poorly with TCP’s control loop

## Slide 10: Dealing with Asymmetry: Global Congestion-Aware
40G
40G
40G
40G
40G
30G
30G
(UDP)
40G
(TCP)
10G
10G
5G
35G
Global CA > ECMP > Local CA
Scheme | Thrput
ECMP (Local Stateless) | 
Local Cong-Aware | 
Global Cong-Aware | 
60G
50G
70G
Local congestion-awareness can be worse than ECMP

## Slide 11: Global Congestion-Awareness (in Datacenters)
 | Datacenter
Latency | microseconds
Topology | simple, regular
Traffic | volatile, bursty
Challenge
Opportunity
Key Insight:
Use extremely fast, low latency
distributed control
Responsive
Simple & Stable
Notes: Why? Well, a fast distributed control would naturally be very responsive and be able to quickly adapt to changing traffic demands.
At the same time, as I’ll show later, it exploits exactly the good properties of the datacenter --- low latency and simple network topologies --- to enable a simultaneously simple and stable solution.

## Slide 12: CONGA in 1 Slide
L0
L1
L2
Leaf switches (top-of-rack) track congestion to other leaves on different paths in near real-time
Use greedy decisions to minimize bottleneck util
Fast feedback loops between leaf switches, directly in dataplane

## Slide 13: Design Space for Load Balancing

## Slide 14: Conga’s design

## Slide 15: Design
CONGA operates over a standard DC overlay (VXLAN -Virtual Extensible LAN)
Already deployed to virtualize the physical network
H1
H2
H3
H4
H5
H6
H7
L0
L1
L2
H9
H8
H1H9
L0L2
H1H9
L0L2
VXLAN encap.
Notes: CONGA operates over a standard datacenter overlay, like VXLAN, that is used to virtualize the physical network.
I don’t have too much time to spend on overlays, but the basic idea is that there are these standard tunneling mechanisms, such as VXLAN, that are already being deployed in datacenters, and provide an ideal conduit for implementing CONGA.

## Slide 16: Design: Leaf-to-Leaf Feedback
H9
H1
H2
H3
H4
H5
H6
H7
L1
H8
1
2
3
0
Track path-wise congestion metrics (3 bits) between each pair of leaf switches
Congestion-To-Leaf
Table @L0
Dest Leaf
Path
0
1
2
L1
L2
3
Congestion-From-Leaf
Table @L2
Src Leaf
Path
0
1
2
L0
L1
3
L0L2
Path=2
CE=5
5
5
L0
L2
L0L2
Path=2
CE=0
L0L2
Path=2
CE=5
L0L2
Path=2
CE=0
L2L0
FB-Path=2
FB-Metric=5
5
1
1
4
3
7
2
Rate Measurement Module
measures link utilization
pkt.CE  max(pkt.CE, link.util)
CE: congestion extent

## Slide 17: Design: LB Decisions
Send each packet on least congested path
H1
H2
H3
H4
H5
H6
H7
L0
L1
L2
H9
H8
Congestion-To-Leaf
Table @L0
Dest Leaf
Path
0
1
2
L1
L2
3
5
5
1
1
4
3
7
2
1
2
3
0
L0  L1: p* = 3
L0  L2: p* = 0 or 1
flowlet [Kandula et al 2007]

## Slide 18: Flowlets for finer load balancing
The source leaf switch detects flowlets and routes them via the least congested path to the destination using congestion metrics obtained from leaf-to-leaf feedback.

## Slide 19: Flowlet table update
Port # | Valid bit (V) | Age bit (A)
Flowlet Table
Each entry pointed by
a 5-tuple hashed value
When a packet arrives, if valid_bit = 1, the flowlet is active and the packet is sent on the port indicated in the entry. If the entry is not valid, the incoming packet starts a new flowlet.
Each incoming packet resets the age bit. A timer periodically (every T seconds) checks the age bit before setting it. If the age bit is set when the timer checks it, then there have not been any packets for that entry in the last T seconds and the entry times out (the valid bit is set to zero). Note that a single age bit allows us to detect gaps between T and 2T.
A=0
A=1
V=0
A=0
A=1
V=0
Gap = 2T
Gap = T
packet
timeout
A=1
A=1

## Slide 20: Distribution of data bytes across transfer sizes for different flowlet inactivity gaps
- 50% of the bytes are in flows larger than 30MB, but this number reduces to 500KB for “Flowlet (500micro-sec)” – much finer granularity
- Entry of the flowlet table: an output port no., a valid bit, and an age bit.

## Slide 21: Why is this Stable?
Source Leaf
Dest Leaf
Stability usually requires a sophisticated control law (e.g., TeXCP, MPTCP, etc)
Feedback Latency
Adjustment Speed
(flowlet arrivals)
(few microseconds)
Near-zero latency + flowlets  stable
Notes: Observe changes faster than they can happen

## Slide 22: How Far is this from Optimal?
Price of Anarchy
H1
H2
H3
H4
H5
H6
H7
L0
L1
L2
H9
H8
bottleneck routing game
(Banner & Orda, 2007)
Given traffic demands [λij]:
with CONGA
Theorem: PoA of CONGA = 2
Worst-case
Notes: Say PoA: Is the price of uncoordinated decision making

## Slide 23: Implementation
Implemented in silicon for Cisco’s new flagship ACI (Application Centric Infrastructure) datacenter fabric
Scales to over 25,000 non-blocking 10G ports (2-tier Leaf-Spine)
Die area: <2% of chip

## Slide 24: Evaluation
Testbed experiments
64 servers, 10/40G switches
Realistic traffic patterns (enterprise, data-mining)
HDFS benchmark
32x10G
32x10G
40G fabric links
Link Failure
32x10G
32x10G
Large-scale simulations
OMNET++, Linux 2.6.26 TCP
Varying fabric size, link speed, asymmetry
Up to 384-port fabric

## Slide 25: HDFS Benchmark 1TB Write Test, 40 runs
Cloudera hadoop-0.20.2-cdh3u5, 1 NameNode, 63 DataNodes
Link failure has almost no impact with CONGA
no link failure
~2x better than ECMP

## Slide 26: Decouple DC LB & Transport
H1
H2
H3
H4
H5
H6
H7
H8
H9
H1
H2
H3
H4
H5
H6
H7
H8
H9
TX
RX
Big Switch Abstraction
(provided by network)
ingress & egress
(managed by transport)

## Slide 27: Conclusion
CONGA: Globally congestion-aware LB for DC
… implemented in Cisco ACI datacenter fabric
Key takeaways
In-network LB is right for DCs
Low latency is your friend; makes feedback control easy
Notes: Network-based lb is architecturally right
Simple distributed, but hardware accelerate mechanisms are near-optimal